## Slide 1: Experimental Plan
Objective: To evaluate the effectiveness hose streams for exterior offensive structural firefighting
Approach: Real scale, instrumented fire suppression experiments.
Key issues
    Ventilation and flow paths
    Gas Cooling
    Suppression
    Model validation data

## Slide 2: Delaware County (PA) Emergency Services Training Center

## Slide 4: Potential Arrangement

## Slide 5: Potential Arrangement

## Slide 6: Potential Arrangement

## Slide 7: Instrumentation
Thermocouples
Total Heat Flux Sensors
Radiometers
Bi-Directional Probes
IR Video
Video
Water/foam flow rate

## Slide 8: Thermocouples
Used to estimated the gas temperature
Once they get wet, they may no longer be providing data about the gas temperature
Potential Approaches
  Two sets – Bare bead – exposed and bare bead covered with a shield to protect from direct liquid contact
  Two sets – one measuring to the point of suppression, insert another after suppression

## Slide 9: Total Heat Flux & Radiometers
Used to measure the rate of energy transfer in to the surface of the sensor
May be used to monitor the energy from the fire/compartment
Used in pairs can assess convective vs radiative heat transfer components
If covered with water or foam limited value of resulting post suppression data.

## Slide 10: Bi-Directional Probes
Used to determine direction and speed of gas flows.
Rely on a differential pressure sensor and a thermocouple.
Moisture adversely affects measurement.
Water in the pressure tubes – no measurement

## Slide 11: Infrared Video
Can be used to “see” thermal flows
Can be used post test to record energy emission from ceilings, walls and floors within the test structure, post suppression
Can be used post suppression to record energy emission from fuel package

## Slide 12: Video
Multiple cameras used to document experiments.
Used to confirm experimental timeline and events during experiment.
Line of sight needed.

## Slide 13: Video - IR Examples

## Slide 15: Remote Control Monitor

## Slide 16: Water Flow Rate

## Slide 17: Townhouse Fire

## Slide 19: Post Fire

## Slide 23: Spray Density/Area of Influence